## Slide 1: MOR based Fast Frequency Sweep for FELIS
Frederik Quetscher, Erion Gjonaj

## Slide 2: FELIS??

## Slide 3: Problem Description
Direct approach for frequency sweep: solve problem in every relevant frequency
  Large number of resonances in spectrum
  Position and number is a priori unknown
  > Large number of model evaluations necessary (expensive)

## Slide 4: Fast Frequency Sweep
Idea: Solve the problem in some frequencies and cheaply obtain the remaining ones
Aproaches
  Rational interpolation of S-parameters (e.g. in CST)
    Vector fitting
    AAA
  AWE, WCAWE
    Rational ‚tailor series‘ expansions of the weak formulation
  MOR
    Low dimensional solution space for the weak formulation (projection)
  …

## Slide 5: MOR overview (RBM)
Evaluate model in frequencies
Use the field solutions as collums in matrix
Orthogonalize
  QR decomposition:
  SVD (POD):
Assemble operator
Solve:
  EQS with only m dimensions
Residual evaluation: (a priori)
Notes: RBM begriff recherchieren
"Geben Sie hier eine Formel ein."

## Slide 6: Further Features
High automation. Required configuration:
  Frequency range
  Frequency resolution
  Stopping criterion
Adaptive choice of frequencies for full model evaluations
  Successive selection based on residual
Creating does not require to assemble
  (affine decomposition)
Error evaluation with a test set (a posterio)

## Slide 7: Architecture
Felis (C++)
Python
HDD
Petsc write
Custom read
Commands: ZeroMQ

## Slide 8: Results – Resistive Waveguide
Computational cost
4 evaluations with MOR
10…100 evaluations without MOR
Simulation Domain
Beam
Resistive
wall
Waveguide ports (10 TM modes)
Notes: Mor Adaptive

## Slide 9: Results – WG Transition
Port
Port
Resistive Wall
Beam

## Slide 10: Results – WG Transition Mesh

## Slide 11: Results – WG Transition
Notes: Mor Adaptive

## Slide 12: Results – WG Transition
Computational cost
  16 evaluations with MOR
    33s
  1000 evaluations without MOR
    81s
  32s residual computation, communication, …
Notes: Mor Adaptive
81s just felis
139 felis+matrix export

## Slide 13: Results – Cube Cavity

## Slide 14: Results – Cube Cavity
Computational cost
  32 evaluations with MOR
    222s
  1000 evaluations without MOR
    137s
  218s residual computation, communication, …

## Slide 15: Computational overhead
File import and exports
Residual computation
  Large number of matrix vector operations due to ports
  In each regarded frequency 1000
Adaptive frequency selection
  Requires residual computations for each added basis function
    20…100 basis functions

## Slide 16: Outlook
Test with larger models
  Ratio of overhead to actual solving better?
More efficient resiual estimation
  Not always in every frequency (less evaluations)
  Nested MOR (QR decomposition)
  Truncation of the basis matrix (SVD)
  Parallelization
Implementation in C++
  Large number of small matrix vector operation is slow inP
  No imports/exports

## Slide 18: Results - Constriction
Notes: Mor Adaptive

## Slide 19: Results – Square Cavity

## Slide 20: Results - Cubewire
Beam
Port
Port
Resistive Wall
Notes: Mor Adaptive

## Slide 21: Results - Cubewire
Beam
Port
Port
Resistive Wall
Computational cost
4 evaluations with MOR
10… evaluations without MOR
Notes: Mor Adaptive